## Slide 1: ADJUSTMENT OF PARABOLIC MIRROR Al-Abedj Fattima Cristmann Anne
30.07.2025

## Slide 2: Introduction
The significance of parabolic mirror alignment:
  How we did the alignment?
  What is a parabolic mirror?
  Measurement, analysis, results.
Our story
  Opinions, difficulties, any strange phenomenon we noticed
  Achievement, issues, improvement
2/14

## Slide 3: Overview
In this presentation, we will describe our journey in the laboratory, where we had to align a parabolic mirror.
This alignment process provided us with new and interesting insights, not only into the alignment of the mirror itself and the components included in the setup, but also into the analysis of the beam images.
3/14

## Slide 4: Optical setup
HeNe
M1
M2
M3
M4
Parabola
Mirror
f1
f2
Iris 1
Iris 2
Iris 4
Iris 3
D = 11mm
CCD
4/14

## Slide 5
5/14

## Slide 6: Parabolic mirror
A parabolic mirror is a reflective surface that has the shape of a paraboloid. It is designed to focus incoming parallel rays to a single point called the focal point.
This type of mirror eliminates spherical aberration, making it ideal for applications that require high precision focusing.
Parabolic mirrors are used to collect, focus, or direct light, depending on the position of the light source relative to the mirror.
If the light source is placed at the focal point, the mirror reflects the light into a collimated beam; if parallel light rays hit the mirror, they are all reflected toward the focal point.
6/14

## Slide 7: Analysis results
Here,we created a calibration table using the beam values obtained by shifting the camera by 50 um.
7/14

## Slide 8: Analysis results
Here,we identified the peaks for each 50 um step.
8/14

## Slide 9: Analysis results
Here,we generated a more colorful version using the surface plot function, applied to the initial configuration without the 50 um camera shift.
We show this colorful 3D surface plot to visually highlight deviations from the ideal parabolic shape, making any misalignment or deformation immediately apparent without the influence of external camera shifts.
9/14

## Slide 10: Interesting facts
What was the most difficult part:
  The most difficult part of our experiment was obtaining a beam without coma or astigmatism, as it required perfect alignment of the setup, as well as precise angular alignment between the camera and the parabolic mirror.
  We realigned the optical setup many times to gain additional understanding and experience, which led us to “cheat” a little the last time by using an interferometer to correct the astigmatism. This wasn’t necessarily a quick fix-on the contrary, it helped us learn how we could address the problem properly.
10/14

## Slide 11: Interesting facts
How we took care of the difficulties:
  We made sure to address the difficulties with extra attention, identifying exactly where the problem was and how it could be corrected.
  We focused on the issues that arose along the way in order to help us work more accurately in the future and to find quicker solutions in similar situations.
11/14

## Slide 12: Interesting facts
Strange phenomenon we noticed:
  Stray reflection caused by light bouncing off the mirror’s mount.
  The beam sometimes failed to converge at the expected focal point, suggesting slight misalignment.
  Various types of aberrations (coma and astigmatism) led to distorted or elongated beam spots.
  Small changes in the angle of incidence resulted in large deviations in the reflected beam, revealing a high sensitivity to alignment precision.
  We observed unexpected patterns such as rings or fringes.
12/14

## Slide 13: Summary & Conclusion
Our achievements in the laboratory were the following:
  We managed to achieve good focus in the end, along with accurate images suitable for processing.
  We learned how each component works and how to build an efficient optical path.
  We learned how to align the parabolic mirror and how to use and adjust the camera to obtain a clear image.
  We practiced calibrating the acquired images and thoroughly analyzing the beam.
13/14

## Slide 14: THANK YOU FOR YOUR ATTENTION!