## Slide 1: PARABOLA ALIGNMENT TRAINING
21 July - 30 July
Contributions :
1st set-up: Cristian Alexe, Anna Fekete
2nd set-up: Denis Sandu, Emilia Matache
3rd set-up: Denis Sandu, Diana Catana
Data Analysis: Diana Catana
Code Results: Denis Sandu
Presentation: Group C

## Slide 2: Table of Contents 1 2 4 3
Intro
Our setup
Objective
3.1 Mirror Pair
3.2 Beam Expender
3.2.1 Collimation
3.3 Second Mirror Pair
5
6
Beam path optimization
Data Analysis
O.A.P
Insights
Summary
7
8

## Slide 3: INTRODUCTION
It reflects parallel incoming rays (e.g. laser light or a distant star) to a single focal point.
It transforms light from a point source placed in its focus into a collimated beam.
Applications:
Telescopes (to focus starlight)
Laser focusing systems
Satellite dishes
Flashlights or headlights (to project a beam)
No spherical aberration
High light efficiency (high reflectivity)

## Slide 4: 02
Objective
To align a collimated laser beam through:
Beam steering mirrors,
Beam expander (collimator),
Final focusing with Off-Axis Parabolic Mirror (OAP).
To generate a clean, diffraction-limited focal spot on a CMOS sensor.
To diagnose and minimize optical aberrations (e.g. astigmatism).
To document and present your optical configuration and alignment strategy

## Slide 5: The setup
HeNe
CV2
CV1
M1
M2
M3
M4
I1
I2
I3
I4
OAP
Detector

## Slide 6
3.1 First Mirror Pair
HeNe
M2
I2
Place Mirror 1 at 45° using a kinematic mount.
Use 2 irises before and after Mirror 1 → adjust until the beam passes through both centers.
Add Mirror 2 at 45° to the reflected beam.
Verify beam stability over time.
Purpose
Redirect the laser beam along the desired optical axis.
Ensure precise beam steering before reaching the parabolic mirror.

## Slide 7: Beam Expender
110 mm
XYZ Translation Stage
Lens 2 (f = +100 mm)
Lens 1 (f = +10 mm)
Purpose
Expand and collimate
Ensure high-quality, parallel beam

## Slide 8: Second Mirror Pair
Control the angle of incidence with high precision.
Gold Mirror: High-reflectivity, often used for IR – placed first in beam path.
Silver Mirror: Broadband reflective – placed second
The highest broadband reflectivity across the visible and near-IR
Beam quality preservation with minimal phase distortion.
Offers very high reflectivity in IR– ideal for Ti:sapphire or Yb lasers).
Highly resistant to oxidation

## Slide 9: Beam Collimation Check
Shearing Interferometer
Used after aligning CV1 and CV2. Adjusted distance until shear fringes were straight → confirmed beam collimation.

## Slide 10: Role of Irises in the Optical Setup
Why are so important?
Define a straight optical path (beam axis) throughout the setup.
Serve as visual and physical alignment guides for mirrors, lenses, and beam direction
Multiple irises: • After laser → before/after mirrors → before OAP.
Beam passed through the center of every iris
Shear method and beam card to confirm centering.
Makes the angle of incidence predictable and repeatable.
Greatly simplifies the coarse and fine alignment of the OAP – fewer corrections needed later

## Slide 11: Off-axis Parabolic Mirror
It provides access to the focus point without beam obstruction
The alignment is sensitive primarily to angle of incidence, while being robust against lateral beam shifts
Fine alignment:
Iterate small changes in Pitch, Yaw, H, V to:
  Center the beam on the CMOS image sensor.
  Reduce astigmatism in the focal spot
  Maximize intensity and minimize spot diameter

## Slide 12: First setup ( Compact version)

## Slide 13: BEST FOCAL POINT
-z
+z
z0

## Slide 14: FOCAL LENGTH DIAGRAM
f
xo
xi
In general
xi=distance from lens to image
xo=distance from lens to object
f=focal length of imaging lens
In our case
xi=distance from the imaging lens to the camera sensor
xo=distance from lens to lens
f=focal length of imaging lens

## Slide 15: OUT OF FOCUS
FOCUS
FOCUS MAGNIFIED

## Slide 16: Systematic setup (II-nd phase)

## Slide 17: Full setup (III-rd phase) and first focusing trials

## Slide 18: Data Analysis (Initial)
Plot profile on Ox and Oy centered on the focused spot in FIJI
Check symmetry and plug in the scale
Calculate FWHM and parameters
***The symmetry check on different axis helps us evaluate the quality of the in-focus beam (we are almost stigmatic !!)
Desaturated
Added brightness to see airy pattern

## Slide 19: Data Analysis (Initial)
Plot profile on Ox and Oy centered on the focused spot in FIJI
Check symmetry and plug in the scale
Calculate FWHM and parameters
***The symmetry check (peak alignment, FWHM, intensity distribution) on different axis helps us evaluate the quality of the in-focus beam (we are almost stigmatic !!)
Ox
Oy

## Slide 20: Code results
Ox
Oy

## Slide 21: Code results
The beam diameter is the one that includes the outer ring that if formed.
https://www.gophotonics.com/

## Slide 22: Results (summary)

## Slide 23: Opinions & Insights
Precisely aligning the Off-Axis Paraboloid (OAP) height during setup
Identifying and verifying if the beam is trully colimated without the sheering interferometer
Managing time across the training days as a team
Challanges
How we tackled the Difficulties
Verified collimation using visual markers for the beam at different distances.
Collaborated with teammates to double-check spatial alignment and height constraints
Using the techniques taught during the training
Strange/Interesting Phenomena Noticed
Small height changes on the parabola led to large variations in focus quality and made it a bit astigmatic

## Slide 24: Summary
Successfully completed full optical setup with final beam focused into the camera
Achieved stable, repeatable alignment of Off-Axis Paraboloid (OAP) and telescope path
Gained hands-on experience with precision alignment, beam collimation, and troubleshooting
Achievements
Remaining Issues & Areas for Improvement
Documenting alignment steps more clearly would save time in future setups
Learned how critical even small mechanical shifts can be to beam quality
Alignment process was time-consuming — consider using alignment jigs or mounts for repeatability(ex. Collimation)

## Slide 25: Thank you!